It has been said that if you use buried cables, then that is enough protection from lightning. Is this a true statement?

No, it’s because buried cables are also vulnerable to the unpredictable power of lightning.

A buried cable does not have as much protection from induced lightning as one might expect, because underground soil easily transmits an electromagnetic field which occurs during a lightning discharge. Also, the high lightning current that is being discharged to ground by the lightning rod can find its way to the buried cables located in the ground.

| Model | Function & Features |
| --- | --- |
| MDP-24-1 | 4-20mA DC & Pulse signal lines |
| MDM2A-24 | 4-20mA DC & Pulse signal lines with Life monitor function |
| MDPA-24 | 4-20mA DC & Pulse signal lines with Life monitor function and degradation checker |
| MA-100 / 200 | Power supply lines 100-120V or 200-240V AC; 2A |
| MAX-100 / 200 | Power supply lines 100-120V or 200-240V AC; 5A |
| MAA-100 / 200 | Power supply lines 100-120V or 200-240V AC with Life monitor function; 5A |
| MAAC-100 / 200 | Power supply lines 100-120V or 200-240V AC with Life monitor function and surge counter; 5A |

M-System has flexible solutions to meet your specific application and requirements. Consult our Signal Conditioners Data Library. 